## Slide 1
Design a forward feed triple effect evaporator to concentrate X1% w/w caustic soda solution to a product with X2 w/w NaOH. Feed liquor is available at F kg/sec at ToC. Last effect of the evaporator can be connected to an existing vacuum system and operated at a pressure of P kPa (abs). Steam with negligible superheat is available at 120oC. Estimated overall heat transfer coefficients for the effects are 3000, 2000 and 1250 W/(m2C), defined with respect to the difference in temperature of the liquid in the effect and the condensing temperature of steam/vapour heating it.
Estimate:
Steam consumption
Heat load
Heat transfer area, Operating temperature, Pressure and Condensate temperature in each effect.

## Slide 2
Group No | X1 | X2 | F | T | P
1 | 10 | 40 | 3 | 60 | 7
2 | 10 | 40 | 4 | 60 | 7
3 | 10 | 40 | 7 | 60 | 7
4 | 10 | 40 | 8 | 60 | 7
5 | 15 | 45 | 3 | 60 | 7
6 | 15 | 45 | 4 | 60 | 7
7 | 15 | 45 | 5 | 60 | 7
8 | 15 | 45 | 6 | 60 | 7
9 | 15 | 45 | 7 | 60 | 7
10 | 5 | 35 | 3 | 50 | 10
11 | 5 | 35 | 4 | 50 | 10
12 | 5 | 35 | 5 | 50 | 10
13 | 5 | 35 | 6 | 50 | 10
14 | 5 | 35 | 7 | 50 | 10
15 | 5 | 35 | 8 | 50 | 10

## Slide 3
Group No | X1 | X2 | F | T | P
16 | 10 | 40 | 3 | 55 | 10
17 | 10 | 40 | 4 | 55 | 10
18 | 10 | 40 | 7 | 55 | 10
19 | 10 | 40 | 8 | 55 | 10
20 | 15 | 45 | 10 | 60 | 7
21 | 15 | 45 | 12 | 60 | 12
22 | 15 | 40 | 6 | 60 | 12
23 | 15 | 40 | 8 | 60 | 12
24 | 15 | 40 | 10 | 60 | 12