## Slide 1: Double Pipe Heat Exchanger Design

## Slide 2: Typical construction
Concentric pipes fitted with packing glands and Tee – joint.
Multiple heat exchangers are connected with return bend and return head
Ref – Process Heat transfer by DQ Kern

## Slide 3: Packing glands and Tee joint
Ref: https://slideplayer.com/slide/11960513/,
https://www.brighthubengineering.com/marine-engines-machinery/65856-a-guide-to-gland-packing-part-two/
Packing glands
Tee joint

## Slide 4: Typical commercial DHE

## Slide 5: Configuration of inner tubes
Ref: https://www.energy-xprt.com/products/hairpin-heat-exchangers-66191
Double pipe heat exchanger design, MED, KAU

## Slide 6: Hairpin Heat exchanger
It’s like a single-pass Shell &Tube unit that has been folded in half to give it a hairpin appearance.
For following conditions these can be an alternative to S&T exchangers:
  Duty < 500 kW
  Low Flow rates
  Large Temperature cross
  Diameter of S&T exchanger is 8" (200 mm) or less.

## Slide 7: Pros and Cons

## Slide 8: Points to ponder
Single tube DPHE
  Shell tube size range - 50 - 150 mm (2” - 4”)
  Inner tube size range - 19 - 65 mm (3/4” - 2.5”)
Multi tubular DPHE
  No of tubes – commonly 7 but can go up to 64
  Shell tube size range – 150 to 200 mm
Finned tube DPHE
  Fins can provide about 2.5 times the external surface area
  hshell < 0.75 htube

## Slide 9: Data Sheet

## Slide 10: Shell and tube side fluids
Shell Side | Tube Side
High Temperature fluid | More viscous fluid
Dirty and fouling fluids | Liquid with lower flow rate
More hazardous or expensive fluid | Fluid undergoing phase change e.g. condensing steam/vapor
Corrosive fluid | Fluid with large ∆T (>40oC)
Streams with low flow rates | Fluid for which pressure drop limit is lower
 | Fluid that has poorer heat transfer characteristics

## Slide 11: Design Considerations
HEs shall be designed to conform to specified shell side or tube side design pressure drop
  Pdesign, min should be 10% above Poperating, max
  Maximum operating pressures
    Shell side – 165 bar
    Tube side – 1033 bar
Tube elements shall be removable without cutting the shell or connecting piping and without disconnecting the shell piping.

## Slide 12: Typical design problem
Known data pf two fluid streams
  Hot fluid –Th,i , flow rate - Known
  Cold fluid – Tc,i , flow rate -
  Design target variables could be - Th,o and/or Tc,o
  Properties
  Allowable ΔP
  Any other restrictions
HE need to be designed

## Slide 13: Key steps in design calculations
Calculate heat duty
Heat transfer area will be calculated with a assumed U value
To achieve this area, inner pipes and outer(shell) pipe sizes will be decided (USE TEMA guidelines)
Cross check
  U calculated should be close to U assumed
  Selected tubes (inner and shell) with the given flow rates satisfied the given ΔP limits?
If both conditioned satisfied – satisfactory design, else - reiterate

## Slide 14: TEMA guidelines
Ref: http://www.thermopedia.com/content/705/

## Slide 15: Double pipe hairpin section data
Ref: http://www.thermopedia.com/content/705/

## Slide 16: Multi tubular hairpins

## Slide 17: Multi tubular hairpins

## Slide 18
(3) Caloric temperatures Tc , tc
If the temperature difference is 50 and viscosity is less than 1 cp, Tc , tc can be taken as average temperatures

## Slide 20
(4) Decide tube side and shell side fluid streams
(5) Estimate the tube side and shell side heat transfer coefficients using the correlations
Calculate jH from the Figure 24 in the data book

## Slide 23
Estimate overall heat transfer coefficient
Since conductive resistance offered by pipe is less, it can be neglected.
U based OD of inner pipe is calculated + Rd

## Slide 25
Entrance and exit losses, one velocity head per hair pin =

## Slide 26: Check
Calculated ΔP (for both tube side and shell side) should be with in the limits.
If this condition doesn’t satisfy we need use series-parallel combinations of hairpins.

## Slide 27
Pressure drop came to be 60 psi in the tube side

## Slide 30
Pressure drop due elevation difference between inlet and outlet should also be included

## Slide 31: References
Process Heat transfer by D Q Kern