## Slide 1: Evaporator design
Week -4
By
Dr.Swambabu Varanasi
Dr. Koustav Ray

## Slide 2: Quick review
Double pipe HE is economically beneficial when required heat transfer area less than 50 m2.
Finned double pipe HE is used when hshell < 0.75 htube
Criteria and methodology used is similar for both except
  equivalent diameter calculations O
  Outer surface area consideration for calculating Uo
Key aspects
  Shell side and tube side streams, Caloric temperature estimation
  Usage of appropriate correlations
  TEMA guidelines
  Reading heat transfer data tables, graphs, etc

## Slide 3: Evaporation
Evaporation is the removal of solvent as vapor from a solution.
Applications
  To concentrate the solutions like sugar syrup, fruit juice, paper mill effluents, caustic soda lye, urea solution, etc.
  To produce crystals in case of evaporative crystallization like ammonium sulfate crystals, salt, etc..
How do we remove solvent from a solutions?
  Heating the solution
  By applying vacuum
  Combined – Usual procedure

## Slide 4: Evaporation system
Is this possible (practically) ?
  Can vapours enter the vacuum generator directly?
    No, vapour disengagement space need to be provided
    Vapours should be condensed
  Flowability of the concentrated solution?
Feed
Heat exchanger
Vacuum
generator
Concentrated
Product

## Slide 5: One possible arrangement – natural circulation evaporator
Feed
Heat exchanger
Vacuum
generator
Concentrated
Product
Condensed
vapours
Condenser

## Slide 6: Another possible arrangement – Forced circulation
Feed
Heat exchanger
Vacuum
generator
Concentrated
Product
Condensed
vapours
Condenser

## Slide 7: Short tube Calandria type evaporator
Image from - http://eacharya.inflibnet.ac.in/data-server/eacharya-documents/55daa452e41301c73a2cb5ac_INFIEP_208/386/ET/5.html and thermopedia

## Slide 9: Basket type evaporator
Image from lixingtitanium.com/info/hanging-baskets-evaporator-2255721.html

## Slide 10: Film-type evaporator
Climbing film evaporator
Falling film evaporator

## Slide 11: Agitated Thin Film Evaporator

## Slide 12: Another possible arrangement – Forced circulation
Feed
Heat exchanger
Vacuum
generator
Concentrated
Product
Condensed
vapours
Condenser

## Slide 13: Flash Evaporator

## Slide 14: Forced circulation evaporator
Image from - http://eacharya.inflibnet.ac.in/data-server/eacharya-documents/55daa452e41301c73a2cb5ac_INFIEP_208/386/ET/5.html

## Slide 15: Gasketed Plate Evaporator

## Slide 16: Direct contact evaporator

## Slide 17: Criteria for evaporator selection

## Slide 18: Evaporator performance
Thermodynamic efficiency of an evaporator is low like a distillation column
‘Steam economy’ or ‘economy’ is used to evaluate the performance of an evaporator
Economy =
Economy can be improved
  Multiple effects
  Vapour compression

## Slide 19: Multiple effect evaporator
Feed forward
Feed backward
Parallel Feed
Mixed feed backward

## Slide 21: Optimum number of effects

## Slide 22: Evaporator design
It should
effectively transfer heat at a high rate with minimum surface area
effectively separate vapour from liquid concentrate
meet solvent evaporation capacity
meet product quality (concentration)
be energy efficient by effective use of steam in multiple-effect evaporation or vapour recompression, wherever possible
minimize fouling of heat transfer surface
be constructed of materials that are adequate to minimize corrosion

## Slide 23: Single effect evaporation
Mass and Energy balance
Where Tcon = steam condensate T
T is the bulk liquid temperature

## Slide 24: Boiling point Elevation
BPE

## Slide 25: Overall heat transfer coefficient
Badger and Shepard (AIChE Trans. 13(I):101-137(1920)) for 30”diameter evaporator with 24 numbers of 2” diameter 48”long tubes

## Slide 26: Multiple effect evaporator

## Slide 27: Design input
Feed rate (F), feed conditions (xF, TF) and desired product concentration (xP)
Pressure (PN) in Nth stage (last effect).
System properties – calculation procedure and / or tables for saturation temperature of solvent (water: steam tables), BPE, enthalpy of solution and solution properties.
Steam supply pressure and temperature (Psteam and Tsteam). Usually Tsteam will have a few degrees of superheat.
Evaporator type & configuration and the estimated heat transfer coefficient of each effect (U1, U2,...UN).

## Slide 28: Design solution
Design objective
  Meeting the final product concentration with high steam economy is the foremost objective.
  The multiple effect evaporator design (triple effect) with same heat transfer area for each effect.
  This is an indirect way to economise on fabrication cost and minimise inventory cost by holding common spares
Design deliverable:
  The heat transfer areas (Ai , i=1,...,N)
  all variables not specified as design input

## Slide 30
Note the inputs: N, F, xF, TF, PN, U1, U2,...UN
Find the value of Ts (PN) from steam table
Estimate LN and Vtotal
Assume Vi = Vtotal / 3
Calculate Li and xi
Estimate BPE from Duhring’s plot
Assuming equal area

## Slide 31
Estimate Temperatures (condensate and products) in each effect
Estimate enthalpy's from steam tables and data tables
Calculate steam and heat load
Calculate based on given overall heat transfer coefficient
Check: see whether assumed condition (equal area) satisfied or not?
Yes – move forward
No -

## Slide 32
Check

## Slide 33
Design a forward feed triple effect evaporator to concentrate X1% w/w caustic soda solution to a product with X2 w/w NaOH. Feed liquor is available at F kg/sec at ToC. Last effect of the evaporator can be connected to an existing vacuum system and operated at a pressure of P kPa (abs). Steam with negligible superheat is available at 120oC. Estimated overall heat transfer coefficients for the effects are 3000, 2000 and 1250 W/(m2C), defined with respect to the difference in temperature of the liquid in the effect and the condensing temperature of steam/vapour heating it.
Estimate:
Steam consumption
Heat load
Heat transfer area, Operating temperature, Pressure and Condensate temperature in each effect.

## Slide 34: Data for assignment question
Steam tables: uploaded to teams (files folder)
or access from:
https://www.nist.gov/system/files/documents/srd/NISTIR5078.htm